Right-of-Way/Street Cut/Excavation Specifications

City of Winchester

1.  Overview

The purpose of this chapter is to ensure the proper procedures, design and construction are followed when cutting into any public street, alley and city owned parking facility or right-of-way. These specifications serve as a guide for contractors and homeowners and are not intended to address every possible situation.  Contractors and homeowners who intend to use alternative specifications and procedures are required to have such approved by the City of Winchester before construction may begin.  The City understands that unique situations may require variances from these specifications and procedures and will provide the necessary guidance and assistance in the best interests of construction and design integrity, public health and public safety. In all cases, the latest edition of the Indiana Department of Transportation (INDOT) Standard Specifications will be enforced on city projects. Where there is any apparent conflict between the City and INDOT Standards, the City Standards will hold precedence.

2.  Permit Requirements

Before any excavation or construction may take place within the public right-of-way (street, alley, tree-row, sidewalk, driveway approaches), an application must be made in writing to the City on the Right-of-Way Use/Street Cut/Excavation Permit Application Form and approved by the City.  Sketches of the proposed work shall be furnished with the application as needed. In the event of an emergency, notification will be given to the City at the time repair crews are dispatched.  If work is required outside business hours, the City is to be contacted the following business day at 8:00 A.M. Permits must be kept on-site when right-of-way work is being performed.  If permitting is not on site, work will be stopped and violators will be subject to fines and license suspension.

If a road closure is required a requests for road closure shall be submitted in writing to the Board of Public Works at least 10 days prior to the proposed closing date.

Permittee will be required to sign that they have received a copy of this form.

3.  License and Bond Requirements

Contractors and Homeowners working within the public right-of-way shall have adequate liability and property damage insurance as detailed in § 96.33(B) Insurance Requirements of Title 9 General Regulations of the City Municipal Code of Ordinances.  The City reserves to right to not allow work within the right-of-way until proof of adequate insurance is provided to the City. The City also reserves the right to require each person or entity engaged in work in the City right-of-way to produce a bond as detailed in § 96.33(C) Bond Requirements of Title 9 General Regulations of the City Municipal Code of Ordinances. Applicant shall furnish written Indemnity Agreement as required in § 96.33 (D) Indemnity Agreement of Title 9 General Regulations of the City Municipal Code of Ordinances.

4.  Underground Utilities

Indiana Underground Plant Protection Service (IUPPS), telephone # 1-800-382-5544, must be properly notified prior to the commencement of cutting any public street, alley, city owned parking facility or right-of-way.

5.  Time Restrictions on Work Hours

Adjacent properties shall have access to the abutting street between the hours of 6:00 PM and 8:00 AM unless notice has been given to the property owner and occupant at least 5 days prior to work. On major thoroughfares as designated by the City of Winchester, blocking or altering traffic may be restricted on weekdays between 6:00 AM and 8:15 AM, and between 4:00 PM and 6:00 PM, unless prior approval is given.

6.  Traffic Control

The Permittee shall erect and maintain all necessary signs, barricades, and warning devices required to safely direct traffic over or around work area.

All cuts in pavement area shall be open to at least one lane of traffic at all times except when permittee is working at site.  If road needs to be closed approval must be given by the City of Winchester.  If cut cannot be completed in the working day it shall be temporarily backfilled, or covered with a steel plate of sufficient size and thickness to carry the traffic. If cut cannot be filled or plated it must be barricaded and secured to prevent accidents or injury.  When work is complete and concrete is in place the cut or trench must be plated to allow for traffic flow.

It is the responsibility of the permittee to provide proper plating and barricades.

7.  Street Repair/Street Patching

A.  Cuts in any public street, alley or city owned parking facility must be made using a saw cut in a neat and uniform manner.  Cutting public streets, alleys or city owned parking faculties in any in any other manner is prohibited unless the City of Winchester gives written approval.

B.  Trenches or cuts shall have a minimum of 9 inches on each side of the trench or cut at the top to allow for a stable surface for concrete and asphalt restoration (see attached sheet).

C.  Cuts and trenches must be bedded, filled and compacted to 95% every 6 to 8 inches with #8 stone within 10 inches of the top of the trench or cut in high or heavy traffic areas or within 8 inches of the top of the trench or cut in low to moderate traffic areas.

D.  Cuts and trenches in high or heavy traffic areas must have a minimum of 8 inches of concrete and 2 inches of asphalt when restoring surface.

E. Cuts and trenches in low to moderate traffic areas must have a minimum of 6 inches of concrete and 2 inches of asphalt when restoring surface.

F.  Designation of high or heavy or low to moderate traffic areas shall be the responsibility of the City of Winchester.

G.  Flowable fill may be used when needed if the City of Winchester grants proper authorization.

H.  Bedding for utilities that cannot use stone must still meet concrete and asphalt requirements.

I.  Asphalt restoration must be completed within 30 days unless the City of Winchester, in writing, approves an extension.  If approval is granted the area must be filled with either hot or cold mix until asphalt restoration is complete.  It is the contractors’ responsibility to maintain the area at no cost to the City of Winchester until restoration is complete.

J.  When cuts occur outside the roadway, but within City of Winchester right-of-way the cut must be filled with #8 stone up to 12 inches of the top of cut. The top 12 inches of the cut must be filled with topsoil and compacted. Grass seed shall then be placed in area.

K.  When cuts occur outside the roadway, but within City of Winchester right-of-way the permittee must clean and restore the affected area within 15 days of the cut completion date or as soon as weather conditions are suitable. Reseeding shall be completed within 15 days of the cut completion date or as soon as weather conditions are suitable for sustaining growth.

L.  It is the permittee’s responsibility to insure all extra trench debris is properly disposed of.

M.  Permittee is responsible for any damage caused to public or private property including but not limited to driveways, yards or streets.

8.  Inspections

The City of Winchester must inspect all cut repairs before permit will be closed.

9.  Violations

If any part of this procedure is not followed the City of Winchester may charge a fee for each day the cut or trench is not repaired as stated in City Ordinance §96.34, Section (D).

Right of Way / Street Cut / Excavation Permit Application

City of Winchester

113 E. Washington Street

Winchester, Indiana 47394

Phone: (765) 584-6845 Fax: (765) 584-6171

Cut Location: _____________________________________________________________________

Name: _________________________________________________________________________

Address: ________________________ ________Phone Number: __________________________

Start Date: __________________________________ Estimated End Date: ____________________

Description of Work: __________________________________________________ ___

__________________________________________________________________________________________________________________________________________________________________

Will the Proposed Project Require Right of Way Closure:    YES _____		NO _____

The maintenance project located at _________________ _, Winchester, Indiana, will require right of way closure for a period beginning ________________ and ending ______________.

If work is performed by a company or person(s) other than stated above please provide the following information.

Name: ________________________________________ Phone Number: _____________________

Contact Person: _________________________________ Phone Number: _____________________

Company Address: _________________________________________________________________

The City of Winchester reserves the right to revoke this permit at any time.

Applicant agrees to meet all standards and specifications as provided by the City of Winchester.

Applicant Signature: _______________________________________ Date: ___________________

# Text boxes

For Street Department Use Only

Street Department Superintendent Signature of Approval:______________________________

For Clerk-Treasurer’s Office Use Only

Date: ______________________		Permit Number: _______________

Amount Received: ___________		Received By:_______________________________

Method of Payment: Cash    Check Number: _______